## Slide 1
MLS 301
MEASUREMENT OF RENAL PLASMA FLOW;
CONCENTRATION & DILUTION TEST & DYE EXCRETION TEST.
BY
EKUN.O.A
MEDICAL LABORATORY SCIENCE
COLLEGE OF MEDICINE OF THE UNIVERSITY OF LAGOS
2015

## Slide 2: LECTURE’S OBJECTIVES
At the end of this lecture, students are expected to;
Measure renal plasma flow
Measure renal blood flow
Be able to carry out urine specific gravity and osmolality tests.
Have good understanding of dye excretion tests.

## Slide 3
Basic renal process:
Urine formation begins with the filtration of plasma from the glomerular capillaries into bowman’s space.
This process is termed glomerular filtration.
The filtrate is known as glomerular filtrate.

## Slide 4: Basic renal process
This filtrate is:
(1) cell-free (under normal condition)
(2) protein free
(3) contains all other substances in plasma (except protein) in virtually the same concentrations as in plasma

## Slide 5: Basic renal process
This filtrate is called ultrafiltrate.
As the ultrafiltrate passes through the tubules, the filtrate’s composition is altered by movement of substances from the tubules to the peritubular capillaries and vice versa.

## Slide 6: Basic renal process
The movement of substance from tubular lumen to peritubular capillary plasma is called TUBULAR REABSORPTION.
On the other hand the movement of substance from the peritubular plasma capillary to tubular lumen is called TUBULAR SECRETION OR SECRETION

## Slide 7: Tubular secretion
Thus tubular secretion is the movement of a solute from the cell interior to the lumen.
Thus a substance can gain entrance into the tubule and be excreted in the urine by glomerular filtration or tubular secretion or both.

## Slide 8: Tubular secretion
Thus amount of substance excreted = amount filtered + amount of the substance secreted- amount of the substance reabsorbed.
Hence the following are important;
(1) glomerular filtration
(2) tubular secretion
(3) tubular reabsorption

## Slide 9: Concept of measurement of renal plasma flow
About 20% of plasma that enters the glomerular capillaries are filtered into bowman’s space.
Assuming a substance X is filtered into the bowman’s space, this filtrate has the same concentration of substance X as in the capillary plasma.

## Slide 10: Concept of measurement of renal plasma flow
The filtrate enters the proximal tubule and begins its flow through the rest of the tubule.
Simultaneously, the remaining 80% of the plasma, containing substance X leaves the glomerular capillaries via the efferent arteriole and enters the peritubular capillaries.

## Slide 11: Concept of measurement of renal plasma flow
Let us assume that the tubule can secret 100% of the peritubular capillary of substance ‘X into the tubular lumen but can not reabsorb this same substance ‘x’;

## Slide 12: Concept of measurement of renal plasma flow
Then the combination of glomerular filtration and tubular secretion will be equal to the total plasma concentration of substance x that originally entered the renal artery.
This means that all the plasma that originally entered the renal artery is CLEARED of ALL OF ITS SUBSTANCE X, which leave the body via urine.

## Slide 13: Concept of measurement of renal plasma flow
From this assumption, we note the following;
(1) Substance X is filtered.
(2) All substance X that escaped filtration is secreted.
(3) No substance X is reabsorbed.
Thus all the plasma that enters the kidney PER UNIT TIME IS CLEARED OF ITS SUBSTANCE X.

## Slide 14: Concept of measurement of renal plasma flow
Hence, CLEARANCE OF SUBSTANCE X IS A MEASURE OF RENAL PLASMA FLOW.
An organic anion known as para-amino- hippurate (PAH) is handled like substance X above. Hence PAH is use for this purpose.
Other substance that behave in a similar way is Inulin, it can be administered intravenously.

## Slide 15: MEASUREMENT OF RENAL PLASMA FLOW.
Theoretically, if a substance is completely cleared from the plasma, the clearance rate of that substance is equal to the total renal plasma flow.

## Slide 16: MEASUREMENT OF RENAL PLASMA FLOW.
This therefore means that the amount of the substance delivered to the kidneys in the blood ( renal plasma flow x plasma concentration of that substance) would be equal to the amount excreted in the urine (urine concentration of that substance x the urine volume).

## Slide 17: MEASUREMENT OF RENAL PLASMA FLOW.
Then renal plasma flow (RPF) can be calculated as:
RPF = Us x V = Cs
Ps
Where;
Us = urine concentration of the particular substance
V = Urine volume
Ps = Plasma concentration of the particular substance
Cs = Clearance of the particular substance

## Slide 18: MEASUREMENT OF RENAL PLASMA FLOW.
Since GFR is 20% of total plasma flow, it therefore means that for a substance to be completely cleared from the plasma, such a substance must be excreted by;
(1) glomerular filtration
(2) tubular secretion

## Slide 19: MEASUREMENT OF RENAL PLASMA FLOW.
in reality, there is no known substance that is completely cleared by the KIDNEYS.
One of the organic anion that is close to achieving this is PAH.

## Slide 20: MEASUREMENT OF RENAL PLASMA FLOW.
PAH when administered is 90% cleared from the plasma.
Hence clearance of PAH can be used as an approximation of renal plasma flow.

## Slide 21: MEASUREMENT OF RENAL PLASMA FLOW.
Peripheral venous plasma can be used because its PAH concentration is essentially identical to that in the arterial plasma reaching the kidney.
The value obtained should be called the EFFECTIVE RENAL PLASMA FLOW (ERPF) to indicate that the level in RENAL VENOUS PLASMA WAS NOT MEASURED.

## Slide 22: MEASUREMENT OF RENAL PLASMA FLOW.
In human’s ERPF averages about 625ml/min.
Correction for % of PAH that is still in the blood when it leaves kidney can be done by calculating the extraction ratio of PAH ( this is the % of PAH removed from the blood).

## Slide 23: MEASUREMENT OF RENAL PLASMA FLOW.
If 90% of PAH is removed from the blood, then the extraction ratio of PAH is 90/100 =0.9
This can be used for further calculation, thus;
Total renal plasma flow = clearance of PAH
extraction ratio of PAH

## Slide 24
Thus;
effective renal plasma flow-
(ERPF) = UPAH x V = clearance of PAH (CPAH)
PPAH
Where;
UPAH = urine concentration of PAH
V = urine volume
PPAH = plasma concentration of PAH
CPAH = Clearance of PAH

## Slide 25
Relationship between ERPF & ARPF.
Actual renal plasma flow (ARPF) = ERPF
extraction ratio
Measurement of renal blood flow:
To determine renal blood flow, value of 2 factors are necessary, these are;
- renal plasma flow
- % of plasma volume in the blood.
Renal plasma flow: this is measured using PAH clearance.

## Slide 26
% of plasma volume in the blood: this is determined indirectly by using (PCV).
for example if PCV is 45%, then the plasma volume of the blood is 100-45 = 55% i.e 55ml of plasma is present in every 100ml of blood.
Thus renal blood flow is calculated with the values of renal plasma volume and % of plasma in blood by using a formula;
renal blood flow = renal plasma flow
% of plasma in blood

## Slide 27
if renal plasma flow is 630ml/min, and the PCV is 45%, then the renal blood flow is;
630
55
100 = 630 x 100 = 1145.46ml/min
55
Thus renal blood flow = RPF x 1
1-Hct
Where;
RPF = Renal plasma flow

## Slide 28
Hct = Haematocrit.
if RPF =700ml/min & Haematocrit (Hct) is 45%, then;
Renal blood flow = 700 x 1 = 700 x 1
1-0.45 0.55
= 1273 ml/min

## Slide 29
URINE SPECIFIC GRAVITY
this is most often determine as a part of a routine analysis.
Occasionally it is measured on timed specimens after restriction, in which case more exact information is derived.
It is measured using either;
(1) urinometer or
(2) Refractometer
The value observed in an apparently healthy individuals varies greatly with fluid intake and the state of hydration.

## Slide 30
Hence the reference range for a 24hr specimen is between 1.015-1.025.
However after fluid restriction it is > 1.025.
Specific gravity using urinometer
Principle; the urinometer is a hydrometer designed for the measurement of urinary specific gravity when placed in the specimen contained in a cylinder, it sinks to the level characteristic of the specific gravity of the specimen. The value may then be read directly from the calibrations on the stem.

## Slide 31
Specific gravity of urine using refractometer
Principle: the refractive index and the specific gravity of a urine specimen are both related functions of the quantity and type of dissolved substance in the specimen. Each substance contributes differently to the refractives index and also to the specific gravity; however because various urine specimens are likely to contain dissolved substance of similar types and proportions, the refractive index and the specific gravity may be correlated. Increased amounts of abnormal substances such as glucose and protein may partially invalidate the correlation and give specific values that are misleading.

## Slide 32
Specific gravity of urine is a measure of the ability of the renal or kidney to concentrates urine or it ability to conserve water.
It is a measure of solute concentration in the urine. Specific gravity of urine. measures the density of urine relative to the density of water, and in most circumstances density bears a constant relationship to osmolality.
Occasionally there may be a remarkable divergence between osmolality and specific gravity.

## Slide 33
The presence of heavy molecules such as protein, glucose, or iodine containing compound affects the specific gravity of urine substantially more than its osmolality.
Urine osmolality measurement;
this is considered more valid In accessing the concentrating ability of the kidney than specific gravity measurement as this measures osmotic concentration of the urine.
This is because, the water excretion is in part, determined by the osmolality of the fluid compartments of the body.

## Slide 34
Consequently, measurement of urine osmolality, especially as part of concentration test is preferred.
In normal individual, osmolality varies widely depending on the state of hydration.
It falls after excessive intake of fluid to about 50mOsm/kg while in severely restricted fluid intake, concentrations of up to 1200mOsm/kg can be observed.
When on average fluid intake, values of 300-900mOsm/kg are most frequently seen.

## Slide 35
A random urine specimen osmolality after a 12-hr fluid restriction gives an osmolality of 850mOsm/kgH20. this is considered normal.
However in the absence of fluid restriction, an osmolality of 600mOsm/kg water or higher is assumed to be normal.
In chronic progressive renal failure: in this condition, the concentrating ability of the tubules is diminished.
In polyuria due to diabetes insipidus: the urine osmolality is extremely low.

## Slide 36
Dye excretion test
These are lipohilic dyes.
These dyes are cleared in the liver & are excreted into bile as;
Intact parent compound
Both parent compound and its conjugates.
Among commonly used dyes are;
Bromosulfophthalein
Indocyanine green
Rose bengal

## Slide 37
The clearance of these dyes by the liver is very rapid.
it is believed that uptake by hepatocytes is a carrier mediated active transport process.
Thus the elimination of these dyes depend on;
(1) the hepatic blood flow,
patency of the biliary tree,
and hepatic parenchymal function
Excretion of these dyes is a sensitive indicators of the presence of Liver disease.
This however does not differentiate between intra & extra hepatic cholestasis.

## Slide 38
The dye excretion method is used to evaluate patients with suspected liver disorder but without jaundice.
Bromosulfophthalein (BSP) was the most popularly used dye, however it has the following demerits;
Some develop fatal hypersensitivity reaction to BSP.
Some develop nausea, syncope, headache, chills and thrombophlebitis at the site of injection.

## Slide 39
Because of these experiences, dye excretion test by (BSP) has been discontinued.
Indocyanine green (ICG)
This can be used in place of BSP as this has some advantages over BSP which are;
Lower incidence of side effects.
Currently, the ICG excretion test is used for investigation of hepatic blood flow and for prediciting clearance rates of drugs such as LIDOCANE that undego first-pass clearance by liver.

## Slide 40
in apparently healthy individual, ICG clearance value ranges from 6.5-14mL/min/kg.

## Slide 41
Thank you for listening.